## Slide 1: Soft Jellyfish Propulsion Simulation Final Update
By: Robert Marlow and Mark Lee

## Slide 2: Motivation
The Initial motivation to simulate a soft jellyfish was to understand how flexible structures interact with hydrodynamic forces to produce propulsion.
Understanding this propulsion would allow us to optimize the soft jelly’s parameters to create the most efficient design for our simulation

## Slide 3: Overview / Approach
The goal of the project is to model a soft jellyfish robot that propels itself through water by contracting its bell
  Marine robots are increasingly valuable to scientific study and commercial exploration[1]
  Jellyfish are a promising option for locomotion biomimicry because they consume very little energy[2]
Simulate a simple 2D cross section of a jellyfish using rods to connect 5 nodes together

## Slide 4: Past Work
Existing simulations of elastic deformation in actuated soft jelly robots
  Discrete differential geometry seems well-suited to this task
Computationally-heavy methods usually used to model fluid-structure interactions
  Would be cool if we could do it faster
BISMAC Actuated Bell Cross-Section[2]
Detailed fluid simulation in IB2D[4]

## Slide 5: Previous Challenges
No net movement under low-Re drag
  Reciprocal motion cannot produce thrust when Re << 1, per the Scallop Theorem[7]
  Actual jellyfish swim at Re = 150 ~ 500[4], [5]
Implemented high-Re (quadratic) drag[6]
  Initially still no propulsion
  Started to see change by increasing CD (0.42 -> ~100)

## Slide 6: Progress in Results
Simulation now predicts net forward movement
Model simplifications resulted in lower thrust force than nature
  Including farther-field effects like jetting and vortexing would slow computation
Height = 0.08 m
Width = 0.1 m
Thickness = 0.04 m
Timestep = 0.01 s
Nnodes = 5
Bending Stiffness EI = 0.01 N-m/rad
Stretching Stiffness EA = 30 N/m
Bell Density = 1050 kg/m3
Seawater Density = 1025 kg/m3
Drag Coefficient CD = 100
2.5x speed

## Slide 7: Bell Fineness Ratio
Species are generally categorized as prolate (F > 1.0) or oblate (F < 0.5)[1]
  Prolate propulsion dominated by jetting
  Oblate propulsion dominated by vortices
  Oblate species are more efficient
F = 1
F = 0.6
F = 0.4
F = 0.8

## Slide 8: Effects of Contraction Amplitude
At higher amplitudes, arm drag force works against forward movement
  Pulling the arms in this far also costs more wasted energy
Modeled differing levels of contraction uniformity
  In nature, oblate species deform more along the edges and prolate species deform more near the apex[1]
Larger Amplitude
Smaller Amplitude

## Slide 9: Modeling More Phenomena
Simplified assumptions to include jetting thrust
Conservation of momentum:
  Jet velocity calculated from change in area under bell
  Distributed force applied to all nodes
Some Jetting
No Jetting

## Slide 10: Future Progress
Implement a more robust hydrodynamic model that could include
  Modeling the mass of the water inside of the jellyfish’s bell to more accurately simulate the hydrodynamics
  Implement some sort of natural jetting force or some sort of vorticity generation
Increase the number of nodes our model can accurately simulate to create a more wave like motion
Bring this simulation to 3D which would allow for more complicated plate simulations
Non Uniform stiffness/geometry

## Slide 11: References
J. Najem, S. A. Sarles, B. Akle, and D. J. Leo, “Biomimetic jellyfish-inspired underwater vehicle actuated by ionic polymer metal composite actuators,” Smart Mater. Struct., vol. 21, no. 9, p. 094026, Sep. 2012, doi: 10.1088/0964-1726/21/9/094026.
A. Villanueva, C. Smith, and S. Priya, “A biomimetic robotic jellyfish (Robojelly) actuated by shape memory alloy composite actuators,” Bioinspir. Biomim., vol. 6, no. 3, p. 036004, Sep. 2011, doi: 10.1088/1748-3182/6/3/036004.
L. Xiangbin and Y. Junzhi, “Design and simulation of a robotic jellyfish based on mechanical structure drive and adjustment,” in 2015 34th Chinese Control Conference (CCC), Jul. 2015, pp. 5953–5958. doi: 10.1109/ChiCC.2015.7260571.
J. G. Miles and N. A. Battista, “Naut Your Everyday Jellyfish Model: Exploring How Tentacles and Oral Arms Impact Locomotion,” Fluids, vol. 4, no. 3, p. 169, Sep. 2019, doi: 10.3390/fluids4030169.
S. R. Anuszczyk and J. O. Dabiri, “Electromechanical enhancement of live jellyfish for ocean exploration,” Bioinspir. Biomim., vol. 19, no. 2, p. 026018, Mar. 2024, doi: 10.1088/1748-3190/ad277f.
M. K. Jawed and S. Lim, “Discrete Simulation of Slender Structures.” Accessed: Oct. 10, 2025. [Online].
E. M. Purcell, “Life at low Reynolds number,” Am. J. Phys., vol. 45, no. 1, pp. 3–11, Jan. 1977, doi: 10.1119/1.10903.